## Slide 1
Machine files and environment_changes
7
Notes: Deniz: split to another powerpoint file

## Slide 2
Machine files
ESM-Tools recognises in which machine is operating (using the all_machines.yaml) and loads the content of the <machine>.yaml (esm_tools/configs/machines/mistral.yaml) under the computer section of the config python object
Feature variables
name – name given to the HPC
config object
general:
...
computer:
name: mistral
additional_flags: "--men=0”
use_hyperthreading: False
...
accounting: True
...
partitions:
computer:
name: "compute”
cores_per_node: "24”
...
fesom:
...
Have a look at the esm_tools/configs/machines/mistral.yaml
This comes from the mistral.yaml, the computer sections in the configuration files/runscript, and the environment_changes

## Slide 3
Machine files
Feature variables
SBATCH flags – list of featured variables that can be used from the computer section to set SBATCH flags (and their defaults):
exclusive_flag: ”--exclusive"
notification_flag: “--mail_type=<type> --mail_user=<email>”
single_proc_submit_flag: "--ntasks-per-node=1” (calculated automatically by ESM-Tools, based on nproc, nproca/nprocb, omp_num_threads…)
tasks_flag: "--ntasks=@tasks@” (calculated automatically by ESM-Tools, based on nproc, nproca/nprocb, omp_num_threads…)
partition_flag: "--partition=@partition@” (calculated automatically by ESM-Tools with the info from partitions dictionary –next slide-)
nodes_flag: "--nodes=@nodes@” (calculated automatically by ESM-Tools, based on nproc, nproca/nprocb, omp_num_threads…)
time_flag: "--time=${compute_time}” (calculated automatically by ESM-Tools with the info from the experiment time variables -1st day presentation-)
hyperthreading_flag: False
additional_flags: "” (you can use this variable to add more SBATCH flags as a list)
<your_runscript>.yaml
computer:
add_additional_flags:
- "--reservation=esmtools"

## Slide 4
Machine files
Feature variables
accounting – if true, the user is required to define a general.account in the runscript
batch_system – defines with <job_scheduler>.py module ESM-Tools will be importing
sh_interpreter – defines the shebang of the comp-*.sh and the *.run files
partitions – dictionary that defines the partitions available, including the name and the number of cores per node
partition – string use to select the
partition label to be used from
the partitions dictionary
<machine>.yaml
partitions:
<label_for_partition-1>:
name: <actual_name_for_the_--partition_flag_in_sbatch>
cores_per_node: <n_cores_per_node>
<label_for_partition-2>:
name: <actual_name_for_the_--partition_flag_in_sbatch>
cores_per_node: <n_cores_per_node>

## Slide 5
Machine files
Feature variables
module_actions – a list of module actions to be included in the compilation and *.run files (i.e. module load netcdf, module unload netcdf, module purge, etc).
Syntax
Omit the “module” word from the command
Although it has nothing to do with the modules, “source” commands are also accepted here
<machine>.yaml
module_actions:
- "purge”
- ”source /FILE/PATH”
- "load netcdf”

## Slide 6
Machine files
Feature variables
export_vars – a dictionary containing all the variables (and their values) to be exported
Syntax
being a dictionary, export_vars is not allowed to have repeated keys
could be a problem when environments are required to redefine a variable at different points of the script or from different yamls
to overcome this limitation, repetitions of the same variable are allowed if the key is followed by an integer contained inside [(int)]:
<machine>.yaml
export_vars:
A_VAR_TO_BE_EXPORTED: the_value
comp-*.sh or *.run
export A_VAR_TO_BE_EXPORTED=the_value

## Slide 7
Machine files
Feature variables
export_vars – a dictionary containing all the variables (and their values) to be exported
Syntax
being a dictionary, export_vars is not allowed to have repeated keys
could be a problem when environments are required to redefine a variable at different points of the script or from different yamls
to overcome this limitation, repetitions of the same variable are allowed if the key is followed by an integer contained inside [(int)]:
<machine>.yaml
export_vars:
A_VAR_TO_BE_EXPORTED: the_value
A_VAR_TO_BE_EXPORTED[(1)]: $A_VAR_TO_BE_EXPORTED:another_value
comp-*.sh or *.run
export A_VAR_TO_BE_EXPORTED=the_value
export A_VAR_TO_BE_EXPORTED=$A_VAR_TO_BE_EXPORTED:another_value
The index is removed!

## Slide 8
environment_changes
Purpose
Modify the environment defined by the machine file in any section of other configuration files or in the runscript.
Syntax
Define one of the following dictionaries in any section of any yaml file (except the machine yamls):
environment_changes (applied for both compilation and run time)
compiletime_environment_changes (only for compilation)
runtime_environment_changes (only during run time)
Note: this whole syntax might change in the coming year, to a more simple approach (i.e. computer section is used, instead of environment_changes)

## Slide 9
environment_changes
Syntax
The environment_changes dictionaries can contain:
add_module_actions: to expand the module_actions list in the <machine>.yaml
add_export_vars: to expand the export_vars dictionary in the <machine>.yaml (redundant variables will be overwritten by the highest file in the hierarchy)
Any other variable or choose to be resolved at the environment stage (i.e. select a MPI configuration for an MPI choose inside the <machine>.yaml)

## Slide 10
environment_changes
Example
fesom-2.1.yaml
compiletime_environment_changes:
add_export_vars:
taken2from: fesom2_compile
choose_computer.name:
juwels:
add_module_actions:
- "unload ParaStationMPI”
- "load ParaStationMPI/5.4.4-1”
- "load netCDF-Fortran/4.4.5"
comp-fesom-2.1.yaml in Juwels
#<module actions defined in juwels.yaml>
module unload ParaStationMPI
module load ParaStationMPI/5.4.4-1
module load netCDF-Fortran/4.4.5
#<exported variables as defined in the juwels.yaml>
export taken2from="fesom2_compile"

## Slide 11
environment_changes
Coupled setups
compiletime_environment_changes allows for different compilation environments under the same coupled setup (i.e. in AWI-ESM-2, the echam.yaml and the fesom-2.1.yaml both contain compiletime_environment_changes, resulting in different compilation environments during esm_master comp-awiesm-2.1)
The runtime environment for online coupled setups is the result of combining:
  The environment information of the <machine>.yaml
  The environment information contained in the runtime_environment_changes in the component files (i.e. echam.yaml, fesom-2.1.yaml, ...)
  The environment information contained in the runtime_environment_changes in the setup file (awiesm.yaml)

## Slide 12
environment_changes
Coupled setups
To define a general environment_changes for all the components of a setup, include the environment_changes inside the general section of the setup file. This will ignore all the environment_changes defined by the standalone files. It is still possible to add component-specific environment_changes from the component section inside the setup file.